## Slide 1: ECE 721 Project 4 figures
Eric Rotenberg

## Slide 2
tag | conf | retired_value | stride | instance
Stride Value Predictor (SVP)
PCtag, PCindex |  |  |  |  |  |  |  |  | 
value |  |  |  |  |  |  |  |  | 
Instance: speculatively incremented, and repaired during recovery using backward walk of VPQ.
H
T
train or replace at retirement
PCindex
prediction, confidence, VPQ entry # (tail)
allocate and record PCtag and PCindex
computed value from writeback (OOO)
prediction = retired_value + instance*stride
confidence = (hit && (conf == conf_max)) // hit = (tag == PCtag) // (always true if no tag)
tag: full, partial, or none
Value Prediction Queue(VPQ)
(in simulator, can record full PC, but true h/w cost depends on # tag bits used)
If tag match (or no tags): // train
new_stride = (value - retired_value) if (new_stride == stride) {conf += 1 (but saturate)} else {stride = new_stride; conf = 0;} retired_value = value instance -= 1
Else // replace
Initialize: tag = PCtag; conf = 0; retired_value = stride = value; instance = {walk VPQ H to T to determine};
PCtag
==?
PC:
PCtag | PCindex | 00
0
1
2
x
x+1
63
# SVP entries = 2(# index bits) = 2(x-1)
discard (always 00)
depends on # tag bits used
Use int64_t for stride and new_stride (strides are signed).

## Slide 3
First, add the following #define macros in pipeline.h (below the existing IS_xxx() macros):
#define IS_INTALU(flags) ((flags) & (F_ICOMP)) // integer ALU instructions #define IS_FPALU(flags) ((flags) & (F_FCOMP)) // floating-point ALU instructions
Second, here is the eligibility code.
// This function checks value-prediction eligibility. // predINTALU, predFPALU, and predLOAD are all "bool" types, // and are configured to be true or false based on corresponding // simulator arguments being 1 or 0, respectively. bool pipeline_t::eligible(payload_t *pay) {
if (!pay->C_valid)
return(false); // Any instruction without a destination register is ineligible.
// If we reached this point, the instruction has a destination register. if (IS_INTALU(pay->flags)) return(predINTALU); // instr. is INTALU type. It is eligible if predINTALU is configured "true". else if (IS_FPALU(pay->flags)) return(predFPALU); // instr. is FPALU type. It is eligible if predFPALU is configured "true". else if (IS_LOAD(pay->flags) && !IS_AMO(pay->flags)) return(predLOAD); // instr. is a normal LOAD (not rare load-with-reserv). It is eligible if predLOAD is configured "true". else return(false); // instr. is none of the above major types, so it is never eligible }